## Slide 1: Facial Recognition Drawer Unlock System: Phase 02
Elijah Ghaya
Ezra Bakatubia
Jesus Chavez-Espino
Liqa Hasan Zaidi
ITAI 2277

## Slide 2: System Overview & Foundations
Architectural Core: ESP-WHO
Edge AI Framework (ESP-WHO): A comprehensive development framework for AI applications. It leverages the MobileFaceNet model on the ESP32-S3 to perform face detection and recognition locally.
Transfer Learning: Instead of training a model from scratch, we use "One-Shot Learning." The system is pre-trained to understand "human faces" in general, needing only 5–10 samples to recognize a specific user.

## Slide 3: Frameworks, Models, and Datasets
The Datasets: Massive collections like WIDER FACE and VGGFace2 (millions of images). These stay on high-power servers and are never stored on the ESP32.
The Models (The Distilled Knowledge): Small, mathematical files (weights) included in ESP-WHO. think of this as the "intelligence" extracted from the datasets—compact enough to fit in the ESP32-S3's memory.
The Framework (The Toolbox): ESP-WHO provides the structure and functions (like align_face() or enroll_face()) that allow you to use these models effectively in your C++ code.
Component | Dataset | Scale | Purpose
Detection (MTMN) | WIDER FACE | 393k Faces | Enables detection despite masks, glasses, or low light.
Recognition (FR) | VGGFace2 | 3.3M Images | Learns universal facial "deltas" (bone structure, etc).
Alignment | AFW / PASCAL | 1.8k Faces | Finds landmarks (eyes, nose) to "level" the face.

## Slide 4: Models Present in the ESP32-S3
MTMN (Multi-task Cascaded Convolutional Networks)
The MTMN (Multi-task Cascaded Convolutional Networks) model which is used for face detection in ESP-WHO was primarily trained on the WIDER FACE dataset.
Scale: 32,203 images containing 393,703 labeled faces.
Purpose: This dataset features high degrees of variability in scale, pose, and occlusion. This is why the ESP32 can detect a face even if you are wearing a mask, glasses, or standing in poor lighting.
MobileFaceNet
The MobileFaceNet architecture, which generates the 512-bytefeature vector (embedding) we are using, was trained on these two massive datasets:
MS-Celeb-1M: Contains 10 million character images of 100k celebrities. It provides the model with a "deep dictionary" of human facial features.
VGGFace2: Contains 3.31 million images of 9,131 subjects. It is specifically designed to handle large variations in pose and age.
Role in the project: These datasets taught the AI what a "human face" looks like generally, so that when it sees our face, it only needs to learn the specific mathematical differences (the "delta") that make us unique.

## Slide 5: How It Works: Transfer Learning
One-Shot Learning at the Edge
The XIAO ESP32-S3 Sense uses Transfer Learning to recognize you without needing a supercomputer.
Pre-trained Logic: By including #include "fr_forward.h", you load a "brain" that already understands human features (eyes, nose, jawline) based on its "childhood" training on massive datasets such as WIDERFACE and VGGFace2.
Universal Features: Because it knows what a generic human looks like, it doesn't need to relearn what a face looks like—it only needs to learn your unique measurements.
Local Enrollment: When you save your face, you aren't "training" a new model. You are simply giving an "educated" AI a new mathematical key to remember in its PSRAM.

## Slide 6: Data Collection & Engineering Pipeline
The system follows a strict pipeline to convert a camera frame into a secure lock trigger:
Capture: Raw JPEG from the OV2640 sensor.
Preprocessing: Decompression into an RGB888 matrix.
Detection: MTMN identifies the bounding box and 5 facial landmarks.
Alignment: Affine Transformation straightens the face (correcting for head tilt).
Feature Engineering: Conversion into a 512-byte (256-dimension) mathematical feature vector.

## Slide 7: Testing Data Acquisition
We utilized the Labeled Faces in the Wild (LFW) dataset to establish a robust security baseline.
The system was tested against 3,023 samples representing 62 unique individuals.
While team photos will be enrolled via the mobile framework, the LFW set serves as our "Unauthorized" population to test rejection reliability.

## Slide 8: Technical Implementation (Data Collection)
C++ Logic for Face Enrollment
This routine runs on the XIAO ESP32-S3 Sense to populate the local PSRAM database.
// 1. Feature Engineering: Alignment & Embedding Generation // This generates the 512-byte (256 * 2 bytes) feature vector dl_matrix3du_t *aligned_face = dl_matrix3du_alloc(1, 112, 112, 3); if (align_face(net_boxes, image_matrix, aligned_face) == ESP_OK) { // 2. Enrollment (Data Storage in PSRAM) // The model measures Euclidean Distance for future matches int8_t left_sample = enroll_face(&id_list, aligned_face); Serial.printf("Sample Collected. Samples remaining: %d\n", left_sample); }

## Slide 9: Privacy, Ethics, and Validation
Secure Biometric Standards
Local-Only Storage: No images or personal data ever leave the device.
Data Minimization: We store vectors, not photos. It is mathematically impossible to reconstruct a face from the 512-byte hash.
Validation Milestone:
  Splitting: We will use the "Leave-One-Out" cross-validation during testing. Collect 5 samples; test if 4 samples can correctly recognize the 5th.
  Goal: Achieve a False Acceptance Rate (FAR) < 1%.
  Final Output: A face_id_list binary blob saved to Flash memory.

## Slide 10: Data Preprocessing
Technical Goal: Optimizing raw image data for the ESP32-S3’s limited computational resources.
Standardization: Images were resized to a 0.4 ratio, resulting in 1,850 features (pixels) per image.
Detection & Alignment: We utilized a pipeline to detect facial presence and normalize features, which is critical for consistent mathematical encoding.

## Slide 11: Exploratory Data Analysis
Security Metric: We calculated Euclidean Distances between facial encodings to define the boundary between an "Authorized" match and a "Stranger".
Findings: Our analysis shows that unauthorized individuals (strangers) have a distance score distribution primarily between 8 and 16.
Unlock Threshold: We have established a strict Unlock Threshold of 20 to ensure high security and minimize false acceptance.